Mechanics – quick questions

- What is a scalar	quantity which only has magnitude

- What is a vector	quantity which has magnitude and direction

- Define displacement		distance moved in a particular direction

- Define average speed 	average speed=total distance travelled/time taken

- Define instantaneous speed small distance travelled/small interval of time

- Define velocity	velocity = change in displacement/time taken or  change in displacement per unit time or rate of change of displacement (with time)

- Define acceleration	change in velocity /time or rate of change of velocity (with time)

- State the equation linking v,u,a,s. Define terms used 	v2 = u2 +2as

- State the equation linking v,t,u,a. Define terms used	v= u + at

- State the equation linking u,t,a,s. Define terms used 	s = ut + ½ at2

- State Newton’s first law An object continues in its state of rest or uniform velocity unless a resultant force acts on it

- State Newton’s second law The acceleration produced when a resultant force acts on an object α the magnitude of the resultant force and is in the same direction as the force

- What happens to mass at speeds close to the speed of light? Mass increases

- Define the Newton	If a force of 1N  is applied to an object of mass 1kg it gives it an acceleration of 1ms-2

- State the equation linking force, mass and acceleration	F=ma

- Define centre of gravity	point where all the weight of the object appears to act

- What is a couple	2 forces of equal magnitude acting in opposite directions but not along the same straight line

- Define the moment of a force	F x perpendicular distance from pivot to line of action of force

- Define torque of a couple	one  force x perpendicular distance between the forces

- State the principle of moments	for equilibrium, sum of CM about any point = sum of ACM about same point or net moment about any point is zero

- State the conditions needed for equilibrium sum of the moments about any point is zero and the resultant/net force is zero

- Define pressure	 force/ X-sectional area (where F is the force perpendicular to the X-sec area)

- Define density 	mass/volume

- Define the joule	work done when a force of 1N moves its point of application by 1m in the direction of the force

- State the equation for kinetic energy.  Define terms used	Ek  = ½ mv2

- State the equation for potential energy. Define terms used	Ep  =  mgΔh

- Define work  		 force x distance moved in the direction of the force

- Define power          rate of doing work or  rate at which energy is converted or work done/time taken   or  energy converted/time taken

- Define the Watt	a power of 1W is achieved  if 1J of work is done/energy converted every second

- State the equation linking power, velocity + force		`P=Fv

- State the equation to calculate efficiency 	useful work output/ total work input ( x 100 %)  or power out/power in (x 100 %)  or useful energy output/ total energy input (x100%)

- Define thinking distance 	distance travelled while driver is reacting before applying brakes

- Define braking distance 	distance travelled after brakes have been applied until it stops

- Define stopping distance 	thinking distance + braking distance

- State Hooke’s Law	Force is proportional to extension provided elastic limit not exceeded

- Define the force constant Force applied/extension (when Hooke’s law obeyed)

- Distinguish between elastic and plastic behaviour	elastic returns to its original shape and size when load removed – plastic does not return .......etc.

- Explain ductile      	ductile material shows plastic behaviour beyond its elastic limit and can be drawn into thin wires   eg copper; lead

- Explain brittle       	brittle material breaks before it deforms plastically eg glass; cast iron

- Explain polymeric       polymeric materials are in long coiled chains; can undergo much larger strains than other materials; can be elastic eg rubber or ductile eg polythene

- Define stress	 	 force/ X-sec area

- Define strain		extension/original length

- State 2 equations for Young’s Modulus (E)	tensile stress/tensile strain   and   Fl/Ax

- Define elastic limit	force/stress/strain/extension beyond which the material does not return to its original length when load is removed

- Define ultimate tensile strength 	the breaking stress of a material

- State the equation for elastic potential energy stored in a spring    ½ Force x extension or ½ force constant x extension2

- What are the units of:   power (W),   force (N),   pressure (Pa),   density kgm-3,   stress (Pa or Nm-2), strain,   Young’s Modulus (Pa or Nm-2),   energy (J),   moment (Nm),   velocity (ms-1) ,   acceleration(ms-2)  ,  speed (ms-1)  ,  displacement (m),   mass (kg),   weight (N),   “g” (ms-2 or N kg-1)

- What numbers do these prefixes represent: : c; m; μ; n; p   centi  (10-2 ); milli  (10-3 );  micro  (10-6 );  nano  (10-9);   pico  (10-12)

- What numbers do these prefixes represent k; M; G; T   kilo (103 ); mega (106 )   giga  (109 );  tera (1012)

- What is 1cm in m

- What is 1mm in m

- What is 1cm2 in m2

- What is 1mm2 in m2

- What is 1m in cm

- What is 1m in mm

- What is 1cm3 in m3

- What is 1mm3 in m3

- What is 103x105

- What is 106x10-2

- What is104/102

- What is 105/10-3