| 6678/01 |
| --- |
| Edexcel GCE |
| Mechanics |
| Unit M2 |  |
| Advanced Subsidiary / Advanced |
| Time: 1 hour 30 minutes |
| Materials required for the examination Answer Book (AB04) Graph Paper (GP02) Mathematical Formulae | Items included with these question papers Nil |

Candidates may use any calculator EXCEPT those with a facility for symbolic algebra, differentiation and/or integration. Thus candidates may NOT use calculators such as Texas TI 89, TI 92, Casio CFX 9970G, Hewlett Packard HP 48G.

Instructions to Candidates

Full marks may be obtained for answers to ALL questions. In the boxes on the Answer Book provided, write the name of the Examining Body (Edexcel), your Centre Number, Candidate Number, the Unit Title (Mechanics M2), the Paper Reference(6678), your surname, other names and signature. Whenever a numerical value of g is required, take g = 9.8 m s-2.

Information for Candidates

A booklet ‘Mathematical Formulae including Statistical Formulae and Tables’ is provided. This paper has 8 questions.

Advice to Candidates

You must ensure that your answers to parts of questions are clearly numbered. You must show sufficient working to make your methods clear to the Examiner. Answers without working will gain no credit

| N1234 R6081 © 2000 Edexcel Foundation This publication may only be reproduced in accordance with Edexcel copyright policy. Edexcel Foundation is a Registered charity. |  |
| --- | --- |

1.	The vectors i and j are perpendicular unit vectors in a horizontal plane.  A ball of mass 0.5 kg is moving with velocity –20i m s(1 when it is struck by a bat. The bat gives the ball an impulse of (15i + 10j) Ns.

Find, to 3 significant figures, the speed of the ball immediately after it has been struck.

(5 marks)

2.	A bullet of mass 6 grams passes horizontally through a fixed, vertical board.  After the bullet has travelled 2 cm through the board its speed is reduced from 400 m s(1 to 250 m s(1.  The board exerts a constant resistive force on the bullet.

Find, to 3 significant figures, the magnitude of this resistive force.	(5 marks)

3.	At time t seconds, a particle P has position vector r metres relative to a fixed origin O, where

r = (t3 – 3t)i + 4t2j,  t ( 0.

Find

(a)  the velocity of P at time t seconds,	(2 marks)

(b)  the time when P is moving parallel to the vector i + j.	(5 marks)

4.

A uniform ladder, of mass m and length 2a, has one end on rough horizontal ground.  The other end rests against a smooth vertical wall. A man of mass 3m stands at the top of the ladder and the ladder is in equilibrium. The coefficient of friction between the ladder and the ground is , and the ladder makes an angle α with the vertical, as shown in Fig. 1. The ladder is in a vertical plane perpendicular to the wall.

Show that 		(9 marks)

5.  	A straight road is inclined at an angle α to the horizontal, where  A lorry of mass 4800 kg moves up the road at a constant speed of 12 m s(1. The non-gravitational resistance to the motion of the lorry is constant and has magnitude 2000 N.

(a)  Find, in kW to 3 significant figures, the rate of working of the lorry’s engine.	(5 marks)

The road becomes horizontal. The lorry’s engine continues to work at the same rate and the resistance to motion remains the same.

Find

(b)  the acceleration of the lorry immediately after the road becomes horizontal,	(3 marks)

(c)  the maximum speed, in m s(1 to 3 significant figures, at which the lorry will go along the horizontal road.		(3 marks)

6.	A cricket ball is hit from a height of 0.8 m above horizontal ground with a speed of 26 m s(1 at an angle α above the horizontal, where . The motion of the ball is modelled as that of a particle moving freely under gravity.

(a)  Find, to 2 significant figures, the greatest height above the ground reached by the ball.

(4 marks)

When the ball has travelled a horizontal distance of 36 m, it hits a window.

(b)  Find, to 2 significant figures, the height above the ground at which the ball hits the window.

(7 marks)

(c)  State one physical factor which could be taken into account in any refinement of the model which would make it more realistic.	(1 mark)

7.

Fig. 2

A uniform plane lamina ABCDE is formed by joining a uniform square ABDE with a uniform triangular lamina BCD, of the same material, along the side BD, as shown in Fig. 2.  The lengths AB, BC and CD are 18 cm, 15 cm and 15 cm respectively.

(a)  Find the distance of the centre of mass of the lamina from AE. 	(9 marks)

The lamina is freely suspended from B and hangs in equilibrium.

(b)  Find, in degrees to one decimal place, the angle which BD makes with the vertical.

(4 marks)

8.	A particle A of mass m is moving with speed 3u on a smooth horizontal table when it collides directly with a particle B of mass 2m which is moving in the opposite direction with speed u. The direction of motion of A is reversed by the collision. The coefficient of restitution between A and B is e.

(a)  Show that the speed of B immediately after the collision is 	(6 marks)

(b)  Show that 	(3 marks)

Subsequently B hits a wall fixed at right angles to the line of motion of A and B. The coefficient of restitution between B and the wall is . After B rebounds from the wall, there is a further collision between A and B.

(c)  Show that 		(4 marks)

END

BLANK PAGE

# Key to Marking Principles

The total number of marks for each paper is 75.

Method marks (M) are awarded for ‘knowing a method and attempting to apply it’, unless otherwise indicated.

Accuracy marks (A) can only be awarded if the relevant method marks (M) have been earned.

(B) marks are independent of method marks.

Method marks cannot be subdivided.

For misreading which does not alter the character of a question or materially simplify it, deduct two from any A or B marks gained, in that part of the question affected.

All marks are ‘correct answer only’ unless shown, for example, as A1  to indicate that previous wrong working is to be followed through. After a misread the subsequent A marks affected are treated as A   but manifestly absurd answers should never be awarded A marks.

The abbreviation awrt stands for ‘anything which rounds to’.

The abbreviation (1eeoo stands for ‘deduct one mark for every error or omission’.

The abbreviation cso stands for ‘correct solution only’.

EDEXCEL FOUNDATION

Stewart House 32 Russell Square London WC1B 5DN

Telephone 0171-393 4444  Fax 0171-753 4558

# Specimen Paper

Advanced Subsidiary/Advanced Level

General Certificate of Education

Subject   MECHANICS	                                                                                                     Paper No.  M2

| Question number | Scheme | Marks |
| --- | --- | --- |
| 1. |  | 0.5v ( 0.5 ((20i) = 15i + 10j | M1A1 |  |
|  |  | v = 10i + 20j | A1 |  |
|  |  |  | M1A1 | (5) |
| 2. |  |  | M1A1, M1A1 |  |
|  |  | 14600 N | A1 | (5) |
| 3. | (a) | u = (3t2 (3)i + 8tj | M1A1 | (2) |
|  | (b) | 3t2 ( 3 = 8t | M1 |  |
|  |  | 3t2 ( 8t ( 3 = 0 | A1 |  |
|  |  | (3t + 1)(t ( 3) = 0 | M1A1 |  |
|  |  | t = (, 3 t = 3 | A1 | (5) |
| 4. |  |  |  | M1A1 |  |
|  |  |  |  | B1 |  |
|  |  |  |  | M1A1 |  |
|  |  |  |  | A1 |  |
|  |  |  |  | M1M1A1 | (9) |

| Question number | Scheme | Marks |
| --- | --- | --- |
| 5. | (a) |  |  |  | M1A1, A1 |  |
|  |  |  |  | P = 12 ( 4532 W ( 52.2 kW | M1A1 | (5) |
|  | (b) |  |  | 4800a = 4352 ( 2000 | M1A1 |  |
|  |  |  |  | a= 0.49 ms(2 | A1 | (3) |
|  | (c) | Max speed | M1A1 |  |
|  |  | ( 26.1 m s(1 | A1 | (3) |
| 6. | (a) | Initial vertical speed = 100=2gh h ( Ht = 5.1 + 0.8 = 5.9 m | B1 |  |
|  |  |  | M1 |  |
|  |  |  | A1 |  |
|  |  |  | A1 | (4) |
|  | (b) |  | B1 |  |
|  |  | Time to window: 36 = 24t ( t = 1.5 s | M1A1 |  |
|  |  |  | M1A1A1 |  |
|  |  | (4.8 m | A1 | (7) |
|  | (c) | One of, e.g., air resistance; spin of ball; variation in g; wind. | B1 | (1) |

| Question number | Scheme | Marks |
| --- | --- | --- |
| 7. | (a) | Ht of ( | M1 |  |
|  |  | = 12 cm | A1 |  |
|  |  | Area | 324 | 108 | 432 | M1A1 |  |
|  |  | Distance of CM from AE | 9 |  |  | B1B1 |  |
|  |  | 9.324 + 22.108 = 432 | M1A1 |  |
|  |  | = 12.25 cm | A1 | (9) |
|  | (b) |  | Distance of G from BD = 9 cm | B1 |  |
|  |  |  |  | M1A1 |  |
|  |  |  |  | A1 | (4) |

| 8. |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | (a) | 3mu ( 2mu = 2mv ( mv | M1A1 |  |
|  |  | 4eu = w + v | M1A1 |  |
|  |  | Solve | M1A1 | (6) |
|  | (b) |  | M1 A1 |  |
|  |  |  | A1 | (3) |
|  | (c) | Rebound speed of | B1 |  |
|  |  | 2nd collision ( | M1 |  |
|  |  | 1 + 4e ( 16e ( 21 |  |  |
|  |  | 3 ( 12e |  |  |
|  |  |  | M1A1 | (4) |